Padova

STATUS OF BMUON CHAMBERS TRIGGER AND CONTROL ELECTRONICS

ASICS:

- BTI		Bunch and Track Identifier

full performance chip						DONE

5 tested prototypes in PLCC68 ceramic package	TESTED

200 tested pcs in TQFP64 plastic package		TESTED

200 tested dies 						ARRIVED

54000 kgd (tender+production)				6/00-12/01 ! !

- TRACO	Track Correlator

full performance chip 						DONE

50 tested prototypes in QFP240 plastic package	ARRIVED

full performance chip IInd submission			6/00

50 tested prototypes in QFP240 plastic package	9/00

5100 tested pcs in QFP240 (tender+production)	1-12/01 ! !

- TS		Track Sorter

full performance chip but 5V technology (TSS)		DONE

10 TSS prototypes in CQFP ceramic package	ARRIVED

full performance prototype submission			6/00

10 tested prototypes					9/00

2000 tested pcs (tender+production)			1-12/01 ! !

PCBs and Modules:

- BTIM		BTI multichip module

I prototype: 4 BTIs in plastic package 66mm x 24mm

on FR4 substrate 100pins SMT type; 25 pcs			DONE

test with simulated tracks				DONE

irradiation tests in gamma cell 5krad and 10krad	DONE

Steady-State Life test (2000h at 125°C)

MIL-STD-883E Method 1005.8			DONE

irradiation tests (neutrons)				DONE

II prototype: 4 BTI dies on LTCC substrate 50mm x 22mm

80pins SMT type, full performance; 40 pcs		ARRIVED

test with simulated tracks				12/99

irradiation and reliability tests				10/99-7/00

12000 pcs (tender+production)				9/00-3/03 ! !

- CB		Control Board

I prototype with test pulse, clock distribution,

monitoring and JTAG controller; 1 piece			DONE

I prototype test						DONE

II prototype for chamber control during production and

irradiation tests							DONE

Slow Control optical link test				DONE

irradiation tests (neutrons)				5-12/99

full performance board						6/00

test on DTBX						9-12/00

irradiation and reliability tests				9-12/00

260 pcs (tender+production)				1/01-6/02

- BTI BOARD

Ist prototype: 4 BTIs in ceramic package with FIFOs

1 piece								DONE

test with simulated tracks				DONE

II prototype: 2 BTIM (16cm x 1 SL)				DONE

test with simulated tracks				DONE

test on MB96 with cosmics; 3pcs			DONE

test on Q4 with beam					DONE

- PHITRB128	128 channels phi view Trigger Board

full performance with 5V/3.3V mixed power supply	12/99

test with simulated tracks				3/00

test on DTBX						3-9/00

irradiation and reliability tests				4-7/00

1000 pcs (tender+production)				3/01-9/03

- PHITRB32	32 channels phi view Trigger Board

full performance							3/00

test with simulated tracks				6/00

test on DTBX						6-12/00

90 pcs (tender+production)				3/01-3/02

- THETATRB	128 channels theta side Trigger Board

full performance							12/00

test on DTBX						6-12/00

350 pcs (tender+production)				3/01-9/03

- SB		Server Board

I prototype: for TRB test						skipped

II prototype: full performance board				6/00

test on DTBX						9-12/00

irradiation and reliability tests				9-12/00

240 pcs (tender+production)				3/01-9/02

- SCB		Sector Collector Board

Ist prototype of Trigger optical link (PAROLI)	GOING

IInd prototype of Trigger optical link 			12/99

full performance board						6/00

test on DTBX						9-12/00

irradiation and reliability tests				9-12/00

65 pcs (tender+production)				6/01-12/02

- SCR		Slow Control Receiver

full performance board						6/00

test on DTBX						9-12/00				20 pcs (tender+production)				6/03-6/04

Mechanical parts – Minicrate design

- Minicrate 		aluminum profile extrusion				12/99

cooling tests (Trigger and Readout)			3-6/00

MB1 minicrate assembly					6/00

Tender+production					6/01-9/03